## Slide 1: Laboratory Real-time Audio Processing
RTProc Getting Started Workshop
Daniel Haupt
IKS Lecture

## Slide 2: 1 Introduction
Real-time Audio Processing based on Software Framework RTProc 2.0
Software Framework RTProc
  Tool for rapid development of real-time prototypes
Why not Program an Audio Processing Application from Scratch?
  Since that is more effort than time is available in our laboratory!
  Better: Re-use of common functional components
  Better: Follow a specific design/develop process and philosophy
What Lesson to Learned Today
  Create your first audio processing application
  Example: build a stereo panning algorithm

## Slide 3: Development Philosophy
idea
Development Timeline
Algorithm Investigation
High level programming language (Matlab)
Offline Processing
Convenient programming
Inefficient implementation (no real-time execution)
Development Phase I
Real-time Evaluation
Programming lang. C/C++
Optimized computational complexity
Real-time version
Efficient implementation
Difficult programming
Development Phase II
Product Integration
(DSP hardware)
C/C++ or Assembler
Hardware specific Optimization
Even more difficult programming
Development Phase III
Real-time Demonstrator
(PC based)
product
idea

## Slide 4: What Audio Processing Algorithms have in Common
Process Input Samples to Produce Output Samples
Process Input Samples to Produce Output Samples in Real-time
Buffer-by-buffer processing, buffersize
Run core processing function infinite number of times

## Slide 5: Goal of This Workshop
Create Your First Real-time Audio Processing Application
Signal Processing Core Functionality with Graphical User Interface (GUI)
Control & Monitoring
Core Processing
User Interaction
Signal Processing

## Slide 6: What else Will You Learn?
Propagate through typical development phases …
Development Timeline
Matlab
C/C++

## Slide 7: What else is Possible?
.. and we will advice you about what else is possible if desired!
Development Timeline
C/C++
C/C++ + JSCRIPT
C/C++ + Obj-C on iOS

## Slide 8: Part I
The Build Environment

## Slide 9: RTProc Project Distribution
All Files for the Creation of New Audio Processing Algorithms
Located in folder
P:\standalone

## Slide 10: The RTProc Runtime and SDK Environment (I)
RTProc Runtime and SDK (Software Development Kit) Environment
Environment located in subfolder
env-dbg for „debug build“ and env-rls for „release build“

## Slide 11: The RTProc Runtime and SDK Environment (II)
RTProc Runtime and SDK Environment
Runtime environment in subfolder runtime
SDK environment in subfolder sdk

## Slide 12: The RTProc Runtime and SDK Environment (III)
Runtime Environment
Directory contains all Executables and similar, e.g.,
  Audio processing host start scripts
  Dynamic link libraries
  System relevant runtime libraries such as Qt
SDK Environment
Directory contains all Files required for Building Executables, e.g.,
  Static libraries
  System header files
  Templates and code fragments
  Build files

## Slide 13: Files for the Creation of the First Application (I)
The Project Files
Projects located in subfolder project

## Slide 14: Files for the Creation of the First Application (II)
Core Signal Processing Component
Located in folder jvxAuNMyAlgorithm

## Slide 15: Files for the Creation of the First Application (III)
Graphical User Interface (GUI) based on QT Audio Host
Located in folder jvxMyHost

## Slide 16: Part II
Let us start…

## Slide 17: Definition of an Example Project
Real-time Panning for Stereo Rendering
Principle Block Diagram
  Single input channel
  Input distributed to left and right output channel
  Apply gain factor to control perceived steering
Desired Real-time control
  Parameter ANGLE to control steering [in degree]
  Parameter CFAC to control steering depth [0 .. 1.0]

## Slide 18: Remember This?
What will be next…
Version
Version
Version
1
2
3

## Slide 19: First Focus on..
The signal Processing Core Component
Remember: Files organized in folder jvxAuNMyAlgorithm
Take a look inside the project…

## Slide 20: Code Components of the Template Project (II)
Provided Source Code Files
Different sub folders for different purposes
Folder to store Matlab implementation
Folder to store C/C++ implementation
1) „first time algorithm exploration“
2) „towards final realization“
1
2

## Slide 21: Setting up the Template Project (I)
First, Build Your Project Template
Open Visual Studio Command Prompt (64 Bit)
Go to folder
P:\standalone\build-algo

## Slide 22: Setting up the Template Project (II)
Next, Create the Visual Studio Solution
Run cmake build script
compile_algo.bat

## Slide 23: Setting up the Template Project (III)
Open Visual Studio
Double-click new Visual Studio Solution
Project.sln

## Slide 24: Preparation of the Template Project (I)
In Visual Studio
Right-click on the INSTALL project, then select
Erstellen/Build
„Build“ is more than just build!

## Slide 25: Preparation of the Template Project (II)
Let us Review the Build Output

## Slide 26: Preparation of the Template Project (III)
What Happens During Install Procedure
Installation of dynamic library to Runtime
Installation of Hooks for Matlab to Runtime
Installation of static library and header files to SDK
User Project
Runtime Environment
SDK Environment

## Slide 27: Part III
First Matlab Implementation
1

## Slide 28: First Implementation of the New Algorithm in Matlab
Start Matlab Host in the Runtime Environment
Double-click Matlab start script
Runtime Environment

## Slide 29: RTProc Host in Matlab Environment (I)
Matlab Starts and Shows User Options

## Slide 30: RTProc Host in Matlab Environment (II)
Start Offline Host at First: jvxHost('off-audio', '--config', 'config.jvx', '--jvxdir', 'jvxComponents');

## Slide 31: RTProc Host in Matlab Environment (III)
Select Input File

## Slide 32: RTProc Host in Matlab Environment (IV)
Input File is Ready
1
Single channel input
Processing parameters
Waveform
Listen to the music!
2
3
4

## Slide 33: RTProc Host in Matlab Environment (V)
Specify Output Signal
1
Add Channels (here: +2)
Activate Generic Matlab Project
Setup Matlab Callbacks
2
3
„JVX mex call Audio Node“
„jvxAuNMyAlgorithm“

## Slide 34: RTProc Host in Matlab Environment (VI)
Save Configuration
1
„Save“ button
WE NEED TO RESTART THE HOST TO PREPARE THE ENVIRONMENT TO MATCH THE CONFIGURATION FILE!!
Restart host

## Slide 35: RTProc Host in Matlab Environment (VII)
Run Processing Algorithm
Push start
Progress bar indicates progress
2
1

## Slide 36: RTProc Host in Matlab Environment (VIII)
Let us Review the Output
Two additional channels available

## Slide 37: RTProc Host in Matlab Environment (IX)
We may..
Export channels to workspace
Save channel to file
Plot the channels in a separate plot diagram
Listen to the processed output
1
2
3
4

## Slide 38: RTProc Host in Matlab Environment - Explained
What we Actually Did…
Data flow diagram

## Slide 39: RTProc Host in Matlab Environment – Debug (I)
Debugging Signal Processing
Open File in Matlab Editor
2
3
1

## Slide 40: RTProc Host in Matlab Environment – Debug (II)
Setting a Breakpoint
Request to stop in processing callback
Restart processing
1
2

## Slide 41: RTProc Host in Matlab Environment – Debug (II)
Stepping Through the Code

## Slide 42: RTProc Host in Matlab Environment – Debug (III)
How to Cleanly Stop Debugging
1
2

## Slide 43: RTProc Host in Matlab Environment – Left-Right-Panning (I)
Specifying the Processing Configuration
Right place: implementation of callback called before processing starts: jvxStartOffline_local

## Slide 44: RTProc Host in Matlab Environment – Left-Right-Panning (II)
Initialization of Processing Parameters
Add parameter ANGLE and CFAC to global variable inProcessing
Set initial values

## Slide 45: RTProc Host in Matlab Environment – Left-Right-Panning (III)
Modify Signals in Processing Loop
Compute channel specific gain factors
Apply to each channel

## Slide 46: RTProc Host in Matlab Environment – Left-Right-Panning (IV)
Listen to the Output
Use a Headphone!

## Slide 47: RTProc Host in Matlab Environment – Left-Right-Panning (V)
„Circulating“ the Input Source

## Slide 48: RTProc Host in Matlab Environment – Left-Right-Panning (VI)
Listen to the Output
Use a Headphone!

## Slide 49: RTProc Host in Matlab Environment – Left-Right-Panning (VII)
Shutting Down the Host
Just close the figure

## Slide 50: Part IV
Real-time Matlab Implementation
2

## Slide 51: RTProc Matlab Host for Real-time Processing
!! STOP OFFLINE MATLAB HOST BEFORE YOU START THE REAL-TIME HOST !!
Start Real-time Host jvxHost('rt-audio', '--config', 'config.jvx', '--jvxdir', 'jvxComponents');

## Slide 52: RTProc Host in Matlab Environment - Explained
What we Plan to Realize
Data flow diagram

## Slide 53: RTProc Matlab Host for Real-time Processing - Configuration
Real-time Host very Similar to Offline Host
The good thing: we use the same configuration file as before
The bad Thing: we need to configure the audio device
1
2

## Slide 54: RTProc Matlab Host for Real-time Processing – The Used Hardware
Hardware Setup
Soundcard in use: Behringer UCA 202
  2 Input Channels
  2 Output Channels
  Medium Quality Audio I/O
  Low Price!
  ASIO Driver available
  Device to rated as „ok for most applications“

## Slide 55: RTProc Matlab Host for Real-time Processing – Hardware Setup (I)
Configure Technology and Device
Select „JVX ASIO Audio Technology“
Select „BEHRINGER USB AUDIO“
1
2
2 input channels & 2 output channels available

## Slide 56: RTProc Matlab Host for Real-time Processing – Hardware Setup (II)
Let us make Life a Little More Easy
There is no external data source connected to the USB soundcard
Let us use a „file input channel“ instead of a real input channel
1
2

## Slide 57: RTProc Matlab Host for Real-time Processing – Hardware Setup (III)
Choose „Virtual Input Channel“ as Input for Panning
File is listed in „Input Files“
Corresponding channels are listed in „Input Channels“
Only the „virtual input channel“ should be active
1
2
3
Ready for processing

## Slide 58: RTProc Matlab Host for Real-time Processing – Hardware Setup (IV)
Start Processing
Connect a headphone
Push the „start“ button
1
2
Matlab runs in real-time!!

## Slide 59: RTProc Matlab Host for Real-time Processing
Conclusion
Matlab operates in real-time!
Hear some artefacts from time to time due to losses of frames – in case user moves windows around
Artefacts due to lost buffers – which cannot be prevented due to single threading only in Matlab
We better switch to C/C++!!
2
Do not forget to shutdown real-time Matlab host!!

## Slide 60: Part V
Offline C/C++ Implementation
2

## Slide 61: First Implementation of the New Algorithm in C/C++
Start Matlab Host in the Runtime Environment
Double-click Matlab start script
Runtime Environment

## Slide 62: RTProc Host in Matlab Environment, C/C++ Implementation (I)
Start Offline Host at First: jvxHost('off-audio', '--config', 'config.jvx', '--jvxdir', 'jvxComponents');
C/C++ implementation at first to be evaluated within Matlab Environment

## Slide 63: RTProc Host in Matlab Environment, C/C++ Implementation (II)
In Matlab Host, Select C/C++ Version of New Algorithm
Component „My New Algorithm“
Let us see how that links to the project!

## Slide 64: C/C++ Programming Explained (I)
What we Plan to Do
Data flow diagram

## Slide 65: C/C++ Programming Explained (II)
Let us Review some Code
Signal processing functionality encapsulated by C++ class
Processing class derived from existing class CjvxAudioNode

## Slide 66: C/C++ Programming Explained (III)
Inheritance Graph
Class CjvxAuNMyAlgorithm: Place for your Algorithm!
Principally: no need to write a single line of code to start!
System API
Default Implementation: Talkthrough

## Slide 67: C/C++ Programming Explained (IV)
Main Purpose of the CjvxAuNMyAlgorithm class: signal processing
Principle
In Detail
  Slightly modified for higher efficiency

## Slide 68: C/C++ Programming Explained (V)
Let us Review the Core Signal Processing
In function process_st: copy input to output
Need to define only those function deviating from default behavior
How does this integrate into a full signal processing application?
copy input to output

## Slide 69: C/C++ Programming Explained (IV)
Matlab host Driving the Algorithm Component
Data source and data source are Matlab workspace variables

## Slide 70: C/C++ Programming Explained (V)
What are the other Functions Good for?
One callback for each user action based on state machine
„activate“ algorithm
„deactivate“ algorithm

## Slide 71: C/C++ Programming Explained (VI)
RTProc State Machine
States and state transitions
Play-pause-rec
Play-rec
equivalent

## Slide 72: RTProc Host in Matlab Environment, Running the C/C++ Code
Enough Explanations, Let’s Go
Process input signal
Current functionality: talkthrough

## Slide 73: RTProc Host in Matlab Environment, Debugging C/C++ Code (I)
Set Breakpoint
In function process_st(..) by clicking to the breakpoint area
click

## Slide 74: RTProc Host in Matlab Environment, Debugging C/C++ Code (II)
Set Breakpoint
Attach Matlab to Visual Studio

## Slide 75: RTProc Host in Matlab Environment, Debugging C/C++ Code (III)
Running Processing Again
Push start

## Slide 76: RTProc Host in Matlab Environment, Debugging C/C++ Code (IV)
Tada…
Breakpoint is hit, go ahead, step through the code,
  F10: step; F11:step into; F5: continue; Shift-F5: detach

## Slide 77: RTProc Host in Matlab Environment, C/C++ Modifications (I)
Modification I: Let us Rename the Algorithm
We rename it to „My First Left-right-panner“
  File componentEntry.cpp,
Build afterwards

## Slide 78: RTProc Host in Matlab Environment, C/C++ Modifications (II)
Argh, a Compilation Error
Matlab Host „locks“ the algorithm dynamic-link-library
Save & close Matlab host GUI first, compile and restart afterwards

## Slide 79: RTProc Host in Matlab Environment, C/C++ Modifications (III)
New Version of Algorithm Selectable in Matlab Host now!

## Slide 80: RTProc Host in Matlab Environment, C/C++ Modifications (IV)
Actual Implementation of the Left-right-Panning
Code modification in function process_buffer
  Compute left-right-gains
  Apply left-right-gains

## Slide 81: RTProc Host in Matlab Environment, C/C++ Modifications (VI)
Mh, this is not a Perfect Solution yet
Modification of ANGLE requires algorithm rebuild
  Let us use the RTProc property system

## Slide 82: Using the RTProc Property System (I)
How it works
Class CjvxAudioNode derived also from class CjvxProperties

## Slide 83: Using the RTProc Property System (II)
Defining Properties for My Algorithm
RTProc code generation tools: The Property Code Generator (PCG)
Where to find that exports_node.pcg file?

## Slide 84: Using the RTProc Property System (III)
Specification of the Required Parameters
Dedicated but very easy to use text format

## Slide 85: Using the RTProc Property System (IV)
Required Code Change in Our Algorithm (Header File)
Derive from code-generated class to inherit all properties

## Slide 86: Using the RTProc Property System (V)
Required Code Change in Our Algorithm (Source File)
On algorithm activation: allocate and register all properties
On algorithm deactivation: unregister and deallocate all properties

## Slide 87: Using the RTProc Property System (VI)
Property Access Entry Points in Matlab
Access functions generated for all specified properties

## Slide 88: Using the RTProc Property System (VII)
Reading Properties from within Matlab
Get value for ANGLE
  jvxAuNMyAlgorithm.get_audio_property_node_ANGLE;
Get value for CFAC
  jvxAuNMyAlgorithm.get_audio_property_node_CFAC;

## Slide 89: Using the RTProc Property System (VIII)
Writing Properties from within Matlab
Set value for ANGLE
  jvxAuNMyAlgorithm.set_audio_property_node_ANGLE(-90);
Set value for CFAC
  jvxAuNMyAlgorithm.set_audio_property_node_CFAC(0.95);

## Slide 90: Using the RTProc Property System (IX)
Possible to Modify Properties in Real-time?
Of course, just use the real-time version of the host (refer to here)

## Slide 91: Using the RTProc Property System (X)
Here is a Funny Little Code Fragment for Moving Source from Right to Left
Just run it while real-time processing operates!

## Slide 92: Part VI
Highly Efficient C/C++ Implementation
3

## Slide 93: Option I: Use an Existing Host Application (I)
We May Run Our Algorithm in an Existing Host Implementation
Start host by double-clicking
start-jvxRtprocHost

## Slide 94: Option I: Use an Existing Host Application (II)
Hosts Loads all Components by Opening Dynamic Link Libraries

## Slide 95: Option I: Use an Existing Host Application (III)
Select the New Left-right-Panning Algorithm

## Slide 96: Option I: Use an Existing Host Application (IV)
Hardware Configuration Dialog

## Slide 97: Option I: Use an Existing Host Application (V)
Find configuration as we did here

## Slide 98: Option I: Use an Existing Host Application (VI)
Once ready, start Processing

## Slide 99: Option I: Use an Existing Host Application (VII)
How can we modify the ANGLE parameter??
We need to CUSTOMIZE the User Interface!
  Remember the second project?

## Slide 100: Option II: Develop a Customized Host (I)
Principle Idea of the Customized Host
A non-custom host is extended by single "custom widget“

## Slide 101: Option II: Develop a Customized Host (II)
Build Your Custom Host Template
Open Visual Studio Command Prompt
Go to folder
build-host

## Slide 102: Option II: Develop a Customized Host (III)
Create the Visual Studio Solution
Run cmake build script
compile_host.bat

## Slide 103: Option II: Develop a Customized Host (IV)
Open Visual Studio
Double-click new Visual Studio Solution
Project.sln

## Slide 104: Option II: Develop a Customized Host (V)
In Visual Studio
Right-click on the INSTALL project, then select
Erstellen/Build

## Slide 105: Option II: Develop a Customized Host (VI)
The Build Output

## Slide 106: Option II: Develop a Customized Host (VII)
First Version of Customized Host is Ready!
Start by double-click

## Slide 107: Option II: Develop a Customized Host (VIII)
Host Application with Custom User Interface
Looks almost as the non-customized host
Drives only ONE specific algorithm

## Slide 108: Integrate the Required Modifications (I)
Starting the QT Designer
Enter “Designer” in Windows search

## Slide 109: Integrate the Required Modifications (II)
Required in Designer: Elements to set the ANGLE and the CFAC Parameters
Open existing widget project myMainWidget.ui

## Slide 110: Integrate the Required Modifications (III)
Add QLineEdit Instances for Parameter Modifications
Drag-And-Drop form left side selection

## Slide 111: Integrate the Required Modifications (IV)
Give Useful Names for the QLineEdits
Names of QLineEdits will be used in source code later on
  lineEdit_ANGLE and lineEdit_CFAC

## Slide 112: Integrate the Required Modifications (V)
Define Callbacks to Catch User Interaction
Callbacks for user interaction are denoted as „slots“
  Right-click into widget space

## Slide 113: Integrate the Required Modifications (VI)
Provide useful Name for the Slots

## Slide 114: Integrate the Required Modifications (VII)
Link User Interaction Events to Slots

## Slide 115: Integrate the Required Modifications (VIII)
Add Slot Definitions in Source Code (Header)

## Slide 116: Integrate the Required Modifications (IX)
Add Slot Definitions in Source Code (Source File)
Read out QLineEdit, transform content into arithmetic value (double)

## Slide 117: Integrate the Required Modifications (X)
Add Slot Definitions in Source Code (Source File)
Pass the values to signal processing algorithm

## Slide 118: Integrate the Required Modifications (XI)
Final Step: Read Values to View in User Interface (Header File)
Define function inform_update_window

## Slide 119: Integrate the Required Modifications (XII)
Final Step: Read Values to View in User Interface (Source File)
Implement function inform_update_window

## Slide 120: Integrate the Required Modifications (XIII)
Finally: Let us Centralize UI Window Show Management
React to User input by redrawing everything

## Slide 121: Standalone Real-time Host is Complete
We are Done!!!